## Slide 1
Audio Chef
CyberChef, but for audio
Drop a recording in, stack DSP operations into a recipe, and hear the result instantly. Every effect is implemented by hand from its signal-processing derivation.
Signals & Systems course project
Notes: Audio Chef is a browser app with a Python DSP backend. The idea comes from CyberChef: operations are cards you drag into a recipe; they run top to bottom and the output updates as you move sliders.

## Slide 2
What Audio Chef does
Three columns, left to right — the same flow as CyberChef
Operations
14 operations in 6 groups: Clean up, Tone & level, Space, Time & pitch, Voice, Edit. Searchable; drag any one out.
Recipe
Cards run strictly top to bottom. Each has its own sliders, quick-setting chips and a bypass switch. Reorder by dragging.
Output
Input and Output waveforms with spectrograms, A/B switch, Listen Stats, Signal Doctor and Export WAV.
0
DSP libraries — numpy FFTs + our own coefficients
300 ms
Auto-Bake: any change re-processes the audio
9+
input formats (WAV, MP3, FLAC, OGG…) or the mic
16-bit
PCM WAV out, turned down rather than clipped
Notes: Audio can come from a dropped file, a file browser or the microphone recorder. Anything libsndfile can decode works: WAV, MP3, FLAC, OGG/Vorbis, Opus, AIFF, W64, CAF, AU. The hard rule: effects are implemented by hand. Only numpy (rfft/irfft, interp, convolve) and scipy.signal.lfilter to RUN coefficients we derived ourselves. librosa, noisereduce, pedalboard and scipy's filter designers are banned.

## Slide 3
How a bake works
React front end → FastAPI back end → one fold over the recipe
1
Upload
Drop a file or record from the mic; the back end decodes it to mono and stores it.
2
Recipe
Every slider change waits 300 ms, cancels the previous request and sends the recipe.
3
Fold
Each card that is not bypassed runs in order, top to bottom; out-of-range values are clamped.
4
Fit
Peak over 1? The whole buffer is scaled to 0.98 — linear, no distortion.
5
Return
A 16-bit WAV comes back, plus input vs output measurements for Listen Stats.
HOW IT WORKS
Slider or card changes
Wait 300 ms, cancel the old request
Send audio id + recipe to the back end
Run the next card (skip if bypassed)
More cards?
Peak over 1? Scale whole file to 0.98
Return WAV + stats, play it
No
Yes
Notes: Vite proxies /api to the FastAPI server on port 8000. The frontend never hard-codes a control: add a parameter to OPERATIONS and it appears in the UI. The last four bakes are kept so their spectrograms can be fetched by X-Bake-Id. The mono fold happens in audio_io.load_audio.

## Slide 4
The STFT core
The shared engine behind every frequency-domain effect
ENGINE
04
WHAT IT IS
Short-Time Fourier Transform and its inverse, written by hand. Noise removal, speed & pitch, the phase vocoder, voice match and the spectrogram all sit on top of it.
HOW TO USE IT
Nothing to drag in — it runs inside every spectral card.
Watch the file edges: the divisor floor makes them fade in rather than click.
The spectrogram under each waveform is this same STFT, drawn instead of modified.
HOW IT WORKS
Audio in
Cut into 2048-sample frames (75 % overlap)
Multiply each frame by a Hann window
FFT: frame → frequency bins
Effect edits loudness / phase of each bin
Inverse FFT, window again, overlap-add
Audio out
Notes: The periodic Hann (not np.hanning) is what satisfies COLA. Dividing by the window-square sum is the Griffin & Lim least-squares reconstruction when the spectrum has been modified. At the file edges only one tapering window contributes, so the divisor tends to 0; flooring it at half the steady-state value avoids a loud click.

## Slide 5
Noise Remover
Removes steady background hiss, hum and fan noise
CLEAN UP
05
WHAT IT IS
Steady noise sits at about the same level in every frequency band all the time; speech comes and goes. Measure the noise per band, then turn each band down by that much in every frame.
HOW TO USE IT
Drag Noise Remover into the recipe (quick chips: Subtle / Strong / Extreme).
Strength (α) 1–4×; Advanced → “Leave a little behind” is the floor β.
Find the noise → “From a part I mark”, then drag the amber region over a noise-only stretch.
Check the spectrogram: the grey haze between words goes dark.
HOW IT WORKS
Noisy audio in
Split into frames (STFT)
Noise region marked?
Auto: quietest 10 % of each band = noise
Subtract the noise from every band
Smooth over 3 frames, inverse STFT
Clean audio out
No
Yes: average it
Notes: Source: S. F. Boll, Suppression of acoustic noise in speech using spectral subtraction, IEEE Trans. ASSP 1979. The auto profile is a simplified 'minimum statistics' (R. Martin 2001). α > 1 because any one frame's noise sits above its mean half the time. The 3-tap time average cuts the variance of random surviving bins by 3.

## Slide 6
De-clip
Redraws peaks that were sliced flat by recording too loud
CLEAN UP
06
WHAT IT IS
When a recording was too loud, its peaks were cut flat at the converter's limit. De-clip finds each flat top and redraws it as a smooth curve that continues the slopes going in and coming out.
HOW TO USE IT
Drag De-clip in; one control, “Clip level” (80–100 % of the file's peak).
Signal Doctor adds it automatically when it sees flat tops near full scale.
Listen to the loudest words: harsh crackle softens.
HOW IT WORKS
Audio in
Find flat-topped runs near the peak
Clipped run found?
Redraw it as a smooth curve
New peak above 1?
Turn the whole file down to fit
Repaired audio out
Yes
No
Yes
No
Notes: The Hermite basis functions are each 1 in exactly one of the four boundary conditions and 0 in the other three. The slope rising into the flat top carries the curve above the clip level — that is the lost peak being restored. The level is relative to the file's own peak, so a file that was clipped and then turned down is still repaired.

## Slide 7
Silence Remover
Cuts the long pauses out, leaving a short breath in each
CLEAN UP
07
WHAT IT IS
Finds every stretch quieter than a threshold that lasts long enough to be a real pause (not the gap between syllables) and shortens it.
HOW TO USE IT
Drag Silence Remover in; quick chips Gentle / Tight / Jump cut.
Quieter than (dB), Longer than (s), Leave (s).
The output waveform gets shorter; short gaps between words survive.
HOW IT WORKS
Audio in
Measure loudness every 10 ms
Take the next quiet stretch
Longer than min pause?
Cut it, keep a short breath, fade joins
More quiet stretches?
Shorter audio out
Yes
No
No
Yes
Notes: The analysis window (20 ms) is wider than the hop (10 ms), so a single click inside a pause lifts at most two hops. Pauses at the very start or end keep only their inner half.

## Slide 8
Level & DC
Re-centres the waveform on zero, then sets the loudness
TONE & LEVEL
08
WHAT IT IS
Removes a DC offset (a waveform sitting above or below the zero line), then turns the whole file up or down so its loudest peak — or its average loudness — hits a target.
HOW TO USE IT
Drag Level & DC in; quick chips Peak −1 dB / Speech −18 dB / DC only.
Remove DC offset (on/off); Set level by: Loudest peak, Average (RMS) or Don't change.
The output waveform sits on the centre line and fills the panel.
HOW IT WORKS
Audio in
Remove DC on?
Subtract the mean, then DC blocker
Measure peak (or average) level
Gain = target ÷ measured level
Multiply every sample by the gain
Levelled audio out
Yes
No
Notes: Near w = 0, |1 − e^{−jw}| ≈ w and |1 − R e^{−jw}| ≈ sqrt((1−R)² + w²), so |H| = 1/√2 at w_c = 1 − R. Subtracting the mean first means the blocker's start-up transient does not appear. An RMS target can push peaks past full scale; the recipe's final fit_to_full_scale turns the whole file down instead of clipping.

## Slide 9
Equalizer
Bass, mid and treble tone controls — three biquads in series
TONE & LEVEL
09
WHAT IT IS
Like the Bass / Mid / Treble knobs on a stereo. Bass lifts or cuts everything below a corner, Treble everything above one, Mid a bell-shaped band around a centre.
HOW TO USE IT
Drag Equalizer in (default: +6 dB bass, +6 dB treble).
Quick chips Subtle / Strong / Extreme / Telephone.
Advanced: bass corner, mid frequency, mid width Q, treble corner.
Watch the bottom or top band of the spectrogram brighten.
HOW IT WORKS
Audio in
Read Bass / Mid / Treble sliders
Work out the filter coefficients
Bass: low-shelf filter
Mid: bell (peaking) filter
Treble: high-shelf filter
Re-toned audio out
Notes: Source: R. Bristow-Johnson, Cookbook formulae for audio EQ biquad filter coefficients. Shelves use S = 1 (Q = 1/√2), the steepest slope with no bump. The high shelf is the low shelf with z → −z. A negative gain gives the exact inverse of the boost. Shelves rather than bells for bass/treble, because a shelf moves a whole band — which is what people mean by 'more bass'. (The code block condenses eq.py's _design(), peaking() and the lfilter call.)

## Slide 10
Filter
Low-pass, high-pass, band-pass and notch — these remove, not tilt
TONE & LEVEL
10
WHAT IT IS
Low-pass keeps what is below a cutoff (muffled, like through a wall); high-pass the mirror (thin, tinny); band-pass keeps one band (the telephone sound); notch removes one narrow band (mains hum).
HOW TO USE IT
Drag Filter in; Type, Frequency (log slider), Steepness 12–48 dB/oct or Width Q.
Quick chips: Muffled, Telephone, Thin, Rumble cut, Hum notch.
Dashed cutoff lines appear on BOTH spectrograms — past them the Output goes dark.
HOW IT WORKS
Audio in
Read type, cutoff and steepness
Low- or high-pass?
Chain Butterworth sections (steeper = more)
One band-pass or notch section
Run the sections one after another
Filtered audio out
Yes
No
Notes: An 8th-order 50 Hz low-pass written as one polynomial goes unstable in floating point; a cascade of second-order sections does not. Poles are inside the unit circle for 0 < w0 < π and Q > 0, which is why the cutoff is clamped below 0.49 fs. Source: RBJ Cookbook; S. Butterworth 1930.

## Slide 11
Compressor
An automatic volume knob: loud parts down, quiet parts up
TONE & LEVEL
11
WHAT IT IS
Watches how loud the audio has recently been; above the threshold it turns the audio down, more the further over. Auto-makeup then lifts everything so the loudest peak is back where it started.
HOW TO USE IT
Drag Compressor in; quick chips Subtle / Strong / Extreme.
Start squashing at (threshold, dB), Squash ratio (:1), Auto-makeup.
Advanced: attack, release, knee, extra gain.
The waveform turns from spiky into a solid block; crest factor drops in Listen Stats.
HOW IT WORKS
Audio in
Follow the loudness (attack / release)
Over the threshold?
Turn down by the ratio (soft knee)
Leave the gain alone
Apply gain + auto make-up
Evened-out audio
Yes
No
Notes: The attack/release switch makes the recursion nonlinear, so it cannot go through lfilter; block_envelope runs it on 1 ms block peaks (a_B = a^B keeps time constants). A causal follower's attack overshoot, lifted ~20 dB by makeup, became the loudest thing in the file — hence lookahead. The soft knee is a quadratic matching both neighbours in value and slope.

## Slide 12
Echo
Distinct repeats, like shouting across a canyon
SPACE
12
WHAT IT IS
Copies of the sound come back after a fixed delay, each quieter than the last. Delay is the gap between copies; Repeats is how much of each copy survives into the next.
HOW TO USE IT
Drag Echo in; quick chips Slapback / Canyon / Endless.
Delay (s), Repeats (%, max 95), Wet (%).
The waveform shows smaller copies trailing each burst.
HOW IT WORKS
Audio in
Add a copy one delay later, quieter
Copy still audible?
Convolve the audio with the copies
Mix wet echo with the dry sound
Echoed audio out
No
Yes
Notes: g is capped at 0.95; at g = 1 the taps never decay. h[0] = 1 already carries the dry signal, so the mix fades the repeats in. The convolution uses rfft/irfft with both signals padded to at least len(x) + len(h) − 1.

## Slide 13
Reverb
Puts the sound in a room, from a small booth to a cathedral
SPACE
13
WHAT IT IS
Thousands of reflections arrive so close together they blur into one smooth tail. Instead of a recorded room, the impulse response is synthesised and convolved with the input.
HOW TO USE IT
Drag Reverb in; quick chips Small room / Hall / Cathedral.
Room size (%), Tail length (RT60, s), Wet (%).
On the spectrogram the harmonic stripes smear to the right instead of stopping.
HOW IT WORKS
Audio in
Pre-delay: a short silence
Early reflections spaced by room size
Noise tail fading over the RT60 time
Damp the highs, normalise the energy
Convolve, mix wet with dry
Audio in a room
Notes: Early reflections at mutually prime delays never line up into a pitched flutter. The noise is drawn from a fixed seed so every bake of the same settings is identical. Schroeder 1962 is the classic reference for artificial reverberation.

## Slide 14
Speed & Pitch
Change how fast it plays and how high it sounds — separately
TIME & PITCH
14
WHAT IT IS
On tape, speed and pitch move together. Two hand-made building blocks decouple them: resampling (the tape effect) and a phase-vocoder time stretch (length without pitch).
HOW TO USE IT
Drag Speed & Pitch in; quick chips Slow-mo / Fast talk / Tape speed-up / Octave down.
Speed (×), Keep pitch (on = podcast 1.5×, off = tape), Pitch (semitones).
The output waveform is shorter or longer than the input.
HOW IT WORKS
Audio in
Keep pitch on?
Phase vocoder: new length, same pitch
Resample like tape: faster = higher
Pitch shift set?
Stretch by r, then resample by r
Audio out
Yes
No
Yes
No
Notes: Without identity phase locking (only peaks run the phase recursion; other bins keep their offset from the peak) the output was ~4 dB quieter and metallic. Linear interpolation is a crude sinc² low-pass, so speeding far up aliases a little on bright material.

## Slide 15
Phase Vocoder
Chipmunk, monster, robot, whisper — the same magnitudes, a new phase
VOICE
15
WHAT IT IS
Keep how loud each frequency is in each frame (that carries the words), rebuild with a different phase (that carries the pitch).
HOW TO USE IT
Drag Phase Vocoder in; choose Voice (quick chips Chipmunk, Robot, …).
How far (1–12 st) for chipmunk/monster; Robot buzz (40–300 Hz).
Spectrogram: stripes move up/down, snap to even lines (robot) or dissolve (whisper).
HOW IT WORKS
Voice in
Split into frames (STFT)
Keep each bin's loudness (the words)
Pick a voice: chipmunk, monster, robot, whisper
Build new phase: shifted, pulsed or random
Inverse STFT, overlap-add
Changed voice out
Notes: Laroche & Dolson, New phase-vocoder techniques for pitch-shifting, IEEE WASPAA 1999. Starting from the MEASURED phase matters — a linear phase lines every partial up at one instant (a click). Formants move with the harmonics here, which is why +7 st sounds like a chipmunk rather than a soprano.

## Slide 16
Celebrity caricatures
Pitch and formants moved separately — loose impressions, not clones
VOICE
16
WHAT IT IS
Modes of the Phase Vocoder card (Ronaldo, Messi, Trump). Each preset is four numbers — pitch, formant (throat size), tempo, rasp — plus an optional EQ bell.
HOW TO USE IT
Drag Phase Vocoder in and pick a celebrity mode (quick chips Ronaldo / Messi / Trump).
Wet (Advanced) blends with the original before the tempo change.
Your own words, rhythm and accent stay — for real resemblance use Voice Match.
HOW IT WORKS
Voice in
Load preset: pitch, formant, tempo, rasp
Shift the harmonics by the pitch ratio
Reshape the envelope (throat size)
Match energy, add rasp + breath, EQ
Change the tempo
Caricature out
Notes: A person with a higher voice has higher harmonics but formants set by their throat size. Moving both together is the cartoon sound; separating them is what makes these sound like a different person rather than a chipmunk. The card says plainly these are caricatures.

## Slide 17
Voice Match
Move your voice toward another speaker's, learned from one shared script
VOICE
17
WHAT IT IS
You and the target each read the same script once. The two readings are aligned in time; from that pairing the card learns how to move your pitch range and vowel colour toward theirs.
HOW TO USE IT
Load three files: your calibration, their calibration, and the take to convert.
On the take, drag Voice Match in and pick Your calibration / Their calibration.
Pitch (%) and Timbre (%) strengths; quick chips Pitch only / Timbre only / Full.
HOW IT WORKS
Your calibration, theirs, the take
Analyse pitch + tone every 10 ms
Line up both readings in time (DTW)
Store the tone difference per frame
For each take frame: map pitch, find 8 nearest
Correct the tone and resynthesise
Your voice, closer to theirs
Notes: Paired-codebook design in the spirit of Arslan & Talkin 1997 (not a reproduction). The DTW is banded (Sakoe-Chiba) and slope-constrained to [1/2, 2], which lets a whole row be vectorised. Alignment quality is checked against random pairs; bad alignments are rejected. Validated on synthetic source-filter speakers; real-voice resemblance is a listening test, not a pytest claim.

## Slide 18
Cut & Trim · Reverse
Keep a part, cut a part out, or play it backwards
EDIT
18
WHAT IT IS
Two editing cards. Cut & Trim keeps only the selection or removes it and joins the two sides. Reverse plays the whole clip — or only a part — backwards.
HOW TO USE IT
Drag Cut & Trim in; Action = Keep the selection / Cut it out.
Drag the green region on the Input waveform (or type From / To; To = 0 means the end).
Reverse: The whole clip, or Only a part via the violet region.
Region preview plays the span, or 2 s either side of a cut to hear the join.
HOW IT WORKS
Audio + selected region
Reverse card?
Play the region backwards
Keep the selection?
Trim: keep only the selection
Splice: cut it out, join the sides
5 ms fade at every new edge
Edited audio out
Yes
No
Yes
No
Notes: A region is drawn on the ORIGINAL input; if an earlier step changed the duration (editor, speed_pitch) the card warns that the two clocks have diverged.

## Slide 19
Arrange timeline
A multitrack timeline — the mix is simply a sum
EDIT
19
WHAT IT IS
An Arrange tab holds blocks, each a piece of another tab's PROCESSED audio placed at a time with its own volume. The tab's audio is all blocks added together; its recipe then runs on that mix.
HOW TO USE IT
Open an Arrange tab; drag file blocks onto lanes.
Move, trim edges, Alt-drag to copy, S splits at the cursor, per-block volume.
Column 2 is still a recipe — it runs on the mix.
HOW IT WORKS
Arrange tab bakes
Take the next block
Get its tab's processed audio, trim, fade
Set its volume, add it at its start time
More blocks?
Too loud? Turn the whole mix down
Mix → the tab's own recipe
No
Yes
Notes: mix_at sizes the output to the union of base and clip and adds the scaled clip at its offset. Lanes exist only in the UI. A block whose source recipe changes duration shows a warning icon.

## Slide 20
Signal Doctor
Measures what is wrong with a recording and prescribes the recipe to fix it
ANALYSIS
Clipping
→ De-clip
Runs of ≥ 3 samples at ≥ 99.9 % of peak, peak ≥ −1 dBFS; read per channel
Hiss
→ Noise Remover + low-pass
Pauses' noise floor > −60 dBFS and > 50 % of its power above 2 kHz
Mains hum
→ Filter notches, Q = 30
50/60 Hz line and harmonics ≥ 12 dB above the max of their neighbourhood
DC offset
→ Level & DC (DC only)
|mean(x)| > 0.01
Low level
→ Level (+ Compressor if crest > 20 dB)
RMS of active hops < −30 dBFS
Long silences
→ Silence Remover
Pauses ≥ 0.3 s below min(−40, L90 − 30) dB > 20 % of the file
Stereo balance
→ Info only
L/R RMS differ > 3 dB, or correlation < −0.3 (mono fold cancels)
FIX ORDER (ORDER CHANGES THE SOUND)
DC → de-clip → hum → noise → low-pass → silence → compressor → level
HOW TO USE IT
Open Signal Doctor in column 3, read the Original / Processed checklist, press “Fix automatically” — the fixes arrive as ordinary cards you can tweak or bypass.
20
Notes: doctor.diagnose() processes no audio: it measures and returns findings plus one fix recipe in a fixed order. DC first because every later measurement assumes a centred wave; de-clip before any filter smears the flat tops; noise removal before silence detection so the pauses are found; gain last so nothing after it pushes the peak back over. The hum check compares a line's max with the MAX of its neighbourhood, not the median — a median bed flagged ordinary speech as hum.

## Slide 21
Spectrogram & Listen Stats
Seeing what changed: frequency over time, and the numbers before vs after
ANALYSIS
21
WHAT IT IS
A spectrogram under each waveform (time → right, pitch → up, brightness = loudness), and a Listen Stats table comparing input with output: peak, RMS, crest factor, DC, ZCR, spectral centroid.
HOW TO USE IT
Always on: load a file and bake any recipe.
Compare Input and Output spectrograms; Filter steps draw dashed cutoff lines on both.
A/B switch (or press B) jumps between input and output at the same point.
HOW IT WORKS
Input and output audio
Split into frames (STFT)
Loudness of each bin in dB
Group bins into 160 rows, 40 Hz–16 kHz
Colour on a fixed −90…0 dB scale
Measure peak, RMS, crest, DC, ZCR
Spectrograms + Listen Stats
Notes: At 44.1 kHz and N = 2048, 40–80 Hz spans 2 bins while 8–16 kHz spans 372; a linear axis would squash all of speech into a thin strip. Waveforms are not normalised either, for the same reason: level changes must be visible.

## Slide 22
Putting it together
A typical session, start to finish
Bring audio in
Drop a file, browse, or record from the mic (localhost only — getUserMedia needs a secure context).
Diagnose
Signal Doctor lists what is wrong; Fix automatically appends the cards.
Shape the recipe
Drag cards, try quick chips or a preset (Podcast cleanup, Radio voice, Nightcore…). Bypass to compare one step.
Compare
A/B switch or the B key; spectrograms and Listen Stats show what changed.
Export
Export WAV downloads the processed 16-bit file.
Every effect is plain numpy, with its derivation written out in the module docstring.
Notes: Run the backend with python3 run.py from backend/ and the frontend with npm run dev from frontend/, then open http://localhost:5173.